## Slide 1
LAB-1
Introduction to STM32 Nucleo-64 Board & arm Keil Studio Cloud
BECE403E-Embedded System Design Lab

## Slide 2
INTRODUCTION TO STM32 NUCLEO-64
Nucleo Features
STM32L152RE ultra-low-power ARM Cortex-M3 based microcontroller
Two extension connectors: Arduino Uno and ST Morpho
Embedded ST –LINK/V2-1 Debugger/Programmer
Flexible board power supply: 3.3 V, 5 V, 7 - 12 V
User LED (LD2), Two push buttons: USER and RESET
MBED Enabled
Interfaces supported on USB: Virtual COM port, Debug port, Mass storage (USB Disk drive) for drag 'n’ drop programming
2
BECE403E-Embedded Systems Design Lab
LAB - 1

## Slide 3
STM32 Nucleo-64 - Board Details
3
BECE403E-Embedded Systems Design Lab
LAB - 1
Image credit: Zephyr Ref. URL : https://docs.zephyrproject.org/latest/boards/arm/nucleo_l152re/doc/index.html

## Slide 4
STM32 Nucleo-64 - Board Details
3
BECE403E-Embedded Systems Design Lab
LAB - 1
Image credit: Zephyr Ref. URL : https://docs.zephyrproject.org/latest/boards/arm/nucleo_l152re/doc/index.html

## Slide 5
STM32 Nucleo-64 - Pin Details (Arduino Headers)
4
BECE403E-Embedded Systems Design Lab
LAB - 1
Image credit: arm MBED, Ref. URL : https://os.mbed.com/forum/electronics/topic/15346/?page=1#comment-52189

## Slide 6
STM32 Nucleo-64 - Pin Details (Morpho Headers)
4
BECE403E-Embedded Systems Design Lab
LAB - 1
Image credit: arm MBED, Ref. URL : https://os.mbed.com/forum/electronics/topic/15346/?page=1#comment-52189
Pins Legend

## Slide 7
STM32 Nucleo-64 - Pin Details (Morpho Headers)
4
BECE403E-Embedded Systems Design Lab
LAB - 1

## Slide 8
STM32L152RE Microcontroller Features
    Package Type : LQFP64 (Low-profile Quad Flat Package)
    Instruction set Architecture : RISC (Reduced Instruction Set Architecture)
    Data bus size : 32-bit
    Address bus size : 32-bit
    Operating Frequency : 32 MHz max
    Operating Voltage : 1.65 V to 3.6 V
    Program memory (flash) : 512 KB
    Data memory (SRAM) : 80 KB
    Data memory (EEPROM) : 16 KB
    Input/output ports : 51(Port A(16), B(16), C(16), D(1),H(2))
    Timers : 9
    Interrupts : 56
    ADC modules (12-bit) : 21 channels
    PWM modules : 10
    Serial communication : SPI(8), USART(5), I2C(2)
INTRODUCTION TO STM32L152RE
5
BECE403E-Embedded Systems Design Lab
LAB - 1

## Slide 9
STM32L152RE - Architecture
6
BECE403E-Embedded Systems Design Lab
LAB - 1
STM32L152RE – Pin diagram

## Slide 10
INTRODUCTION TO Keil Studio IDE
Keil Studio Cloud is the successor to the Mbed Online Compiler, and allows you to develop Mbed 2, Mbed OS 5 and 6 projects on supported Mbed-enabled boards.
Free to use, browser-based IDE for the evaluation and development of embedded, IoT, and Machine Learning software for Cortex-M devices.
You can compile projects using Arm Compiler 6, run the projects directly on supported development boards, and debug from supported browsers without the need to install any software.
You can access Keil Studio Cloud using an Arm or Mbed account (use below link) and get started by opening a reference design to evaluate.
https://studio.keil.arm.com
1
BECE403E-Embedded Systems Design Lab
LAB - 1

## Slide 11
LAB-1
Working with LED
BECE403E-Embedded Systems Design Lab
7
BECE403E-Embedded Systems Design Lab
LAB - 1

## Slide 12
LAB TASK-1
Blinking of LED on Board
Write a program to blink an on-board LED (LD2) of the STM32 Nucleo-64 board with 0.5s delay between ON and OFF state using Keil Studio Cloud IDE.
8
BECE403E-Embedded Systems Design Lab
LAB - 1

## Slide 13
1
BECE403E-Embedded Systems Design Lab
LAB - 1
ARM Keil Studio Could IDE Demo for Blink LED

## Slide 14
INTRODUCTION TO Keil Studio IDE
Procedure to create a mbed example project
  Go to ARM Keil Studio (https://studio.keil.arm.com/auth/login/) and log in
  Select File → New → Mbed Project
  Click the Example project drop-down list and select “mbed2-example-blinky”
  In Project name field, provide the name of the new project and click Add project
  Double click on the “main.cpp” file from the newly created project folder
  Modify the code in the editor window as per the logic of your application
  Check for any errors in the program under the “Problems” tab of the panels window
  If no errors, connect the Nucleo Board to the computer using Micro USB Cable
  Click Play icon (Run project) to upload and start the code execution on the board.
1
BECE403E-Embedded Systems Design Lab
LAB - 1

## Slide 15
INTRODUCTION TO Keil Studio IDE
Procedure (one-time) to connect Nucleo board to Keil Studio Cloud IDE
  In Side bar, under Build target drop-down list select “NUCLEO-L152RE”
  Then, click on the Connected device option to open the Device Manager
  Connect Nucleo Board to the computer using Micro USB Cable
  Click Add Device button and select device firmware (STLink) and then click Connect
  Nucleo board is now ready to be used to run and debug a project
  After the first successful connection, Keil Studio automatically detects the hardware
1
BECE403E-Embedded Systems Design Lab
LAB - 1

## Slide 16
LAB TASK-1
8
BECE403E-Embedded Systems Design Lab
LAB - 1
API required:
DigitalOut Identifier(PinName) - Used configure GPIO pin as digital output pin
- Identifier: User defined name to access this digital pin
- PinName: Name of the pin as specified in the Nucleo board pin details
- Examples: DigitalOut myled(LED1); //LED1 is an onboard LED
DigitalOut myA3(PC_0); //PC_0 is 0th pin of port C
operator= (int value) - used to set the digital output as 0 or 1. A shorthand for write() API.
  - Example: myA3=1; //set the PC_0 digital output pin value as HIGH or 1
wait(s) – Used to pauses the execution of a program for the amount of time (in seconds)
- s: Float value indicate the number of seconds to pause.
- Example: wait(1.0); //will pause the program for 1 second.
wait(0.5); //will pause the program for 0.5 second

## Slide 17
LAB TASK-1
Program: Output:
10
BECE403E-Embedded Systems Design Lab
LAB - 1

## Slide 18
LAB TASK-2
Blinking of 4 LEDs alternatively in pairs
Write a program to blink four LEDs in alternatively in pairs (1010 and 0101 pattern) with 0.5 Sec delay between each. Implement and verify this logic on the STM32 Nucleo-64 board using Keil Studio Cloud IDE.
11
BECE403E-Embedded Systems Design Lab
LAB - 1

## Slide 19
LAB TASK-1
Program: Connection diagram:
10
BECE403E-Embedded Systems Design Lab
LAB - 1

## Slide 20: THANK YOU
by
prakash v