## Slide 1
LAB-11
Working with 7-Segment Display
BECE403E-Embedded System Design Lab
1
BECE403E-Embedded System Design Lab
LAB-11

## Slide 2
INTRODUCTION TO 7-SEGMENT DISPLAY
Most commonly used displays along with the microcontrollers are LCD, LEDs and seven segment displays etc.,
Seven segment displays are the output display devices that provide a way to display information in the form of alphanumeric characters and digits.
This is most commonly used in many gadgets, and electronic appliances like digital meters, digital clocks, microwave oven and electric stove, etc.
These displays consist of seven segments (indicated as A-G) of light emitting diodes (LEDs) and that is assembled into a structure like numeral 8.
In addition, an extra 8th segment is used to display dot (indicated as H/DP), which is useful while displaying non integer number.
2
BECE403E-Embedded System Design Lab
LAB-11

## Slide 3
INTRODUCTION TO 7-SEGMENT DISPLAY
A seven segment displays are generally available in ten pin package, 8 pins relate to the 8 LEDs, the remaining two pins at middle are internally shorted.
These segments come in two outlines they are common cathode and common anode.
  In common cathode configuration, the all LED’s negative terminals are connected to the common ground pin hence HIGH on corresponding positive pin glow particular LED.
  In a common anode arrangement, the common pin is given to a logic HIGH and the pins of the LED are given LOW to display a number.
3
BECE403E-Embedded System Design Lab
LAB-11

## Slide 4
3
BECE403E-Embedded System Design Lab
LAB-11

## Slide 5
3
BECE403E-Embedded System Design Lab
LAB-11
Hexa Value | Decimal Digit | Individual Segments Illuminated for Common Cathode configuration |  |  |  |  |  |  | 
 |  | dp (PC_7) | g (PC_6) | f (PC_5) | e (PC_4) | d (PC_3) | c (PC_2) | b (PC_1) | a (PC_0)
0x3F | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1
0x06 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0
0x5B | 2 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 1
0x4F | 3 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 1
0x66 | 4 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0
0x6D | 5 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1
0x7D | 6 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 1
0x07 | 7 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1
0x7F | 8 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1
0x6F | 9 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1

## Slide 6
3
BECE403E-Embedded System Design Lab
LAB-11
Hexa Value | Decimal Digit | Individual Segments Illuminated for Common Anode configuration |  |  |  |  |  |  | 
 |  | dp (PC_7) | g (PC_6) | f (PC_5) | e (PC_4) | d (PC_3) | c (PC_2) | b (PC_1) | a (PC_0)
0xC0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0
0xF9 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1
0xA4 | 2 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 0
0xD0 | 3 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0
0x99 | 4 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1
0x92 | 5 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 0
0x82 | 6 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0xF8 | 7 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0
0x80 | 8 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x90 | 9 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0

## Slide 7
LAB TASK-1
Display hexa decimal values from 0 to 9
Write a mbed C++ program to display decimal values from 0 to 9 on the 7-segment display interfaced with digital pins of Nucleo boards. Once the sequence completed from 0 to 9 then repeat the sequence again. Design and implement this logic on the STM 32 Nucleo L152RE board using Keil studio could platform.
Note: Try to perform the display of 0 to F by modifying above program
7
BECE403E-Embedded System Design Lab
LAB-11

## Slide 8
LAB TASK-1
Program Connection diagram
8
BECE403E-Embedded System Design Lab
LAB-11

## Slide 9
LAB TASK-2
Display numbers from 00 to 99
Write a mbed C++ program to display a two digit decimal numbers from 00 to 99 using 7-segment LEDs. Use common digital pins of Nucleo board for both 7-segments LED connection and display the digit using multiplexing logic i.e one digit at a time on each 7-Segment with small delay values (few us). Use a switch to stop the number sequencing. Design and implement this logic on the STM 32 Nucleo L152RE board using Keil studio could platform.
9
BECE403E-Embedded System Design Lab
LAB-11

## Slide 10
LAB TASK-2
10
BECE403E-Embedded System Design Lab
LAB-11
Program

## Slide 11
LAB TASK-2
11
BECE403E-Embedded System Design Lab
LAB-11

## Slide 12
LAB TASK-2
12
BECE403E-Embedded System Design Lab
LAB-11
Connection diagram

## Slide 13
CHALLENGING TASK
Token display system
Write a mbed C++ program to design a token display system which helps to serve the customer with out the need of standing in a queue. This display system consist of one 7-segment display to display token numbers from 0 to 9, and token numbers are received into Nucleo board via 4x3 keypad. Design and implement this logic on the STM 32 Nucleo L152RE board using Keil studio could platform.
13
BECE403E-Embedded System Design Lab
LAB-11

## Slide 14
Challenging Task
14
BECE403E-Embedded System Design Lab
LAB-11
Connection diagram

## Slide 15
CHALLENGING TASK
15
BECE403E-Embedded System Design Lab
LAB-11
Program

## Slide 16: THANK YOU
by
prakash v